# 差动激励下海床-桩-墩-桥体系的地震弹塑性（II）：工程应用与参数敏感性分析

柳国环1，2，等

（1. 天津大学，建筑工程学院，天津，300072；2. 清华大学，土木水利学院，北京，100084）

摘要：首先，建立大跨海床地基-桩-墩-桥结构体系空间数值模型，包括粘弹性人工边界、悬索找形几何非线性、桩-土接触非线性以及钢筋混凝土材料非线性。其次，计算和对比考虑地基和人工边界条件与否的三种结构体系模态。同时，生成地基输入位置的多点地震动。然后，重点在性质考察构件进入塑性对地震输入空间变异性，人工边界条件和接触非线性的敏感性；进而，量化给出拟静力与动力反应贡献比例，认识体系塑性铰出现时间、位置及其分布规律。结果表明：（1）结构体系的水动质量与人工边界条件影响不容忽视；（2）塑性铰对于一致与差动输入敏感，影响分布规律和破坏模式；（3）拟静力影响源于不均匀输入导致的反应不一致性，动力作用影响源于频谱；（4）随地震强度加大，塑性反应对接触非线性的敏感性加强，破坏为严重。

关键词：跨海大桥；粘弹性人工边界；多点地震动；塑性铰；破坏模式；拟静力

Elasto-plasticity Analysis of Bridge Accounting for Spatial Variability of Earthquake Motion and Seabed-pile-piers-bridge Interaction

Part (II): Application and Parameter Sensitivity Analysis

Liu Guohuan1,2，etc

(1. School of Civil Engineering, Tianjin University, Tianjin, 300072; 2.Department of Civil Engineering, Tsinghua University, Beijing, 100084）

Abstract: A three-dimensional finite element model of large-span seabed-pile-piers-bridge is established. In the model, the visco-elastic artificial boundary condition, form-finding of suspension-cable for the geometric nonlinearity, pile-soil contact and material nonlinearity are considered. The modal analysis of the bridge system considering soil and artificial boundary condition or not are conducted and compared. The multiple-point earthquake motions at underground location are generated and verified. Then, the sensitivity analysis about the plastic hinges occurrence and distribution to the variability of spatial earthquake motions, artificial boundary condition and contact nonlinearity are analyzed in detail. While, relative contribution of pseudo-static and dynamic to the total response are analyzed and given. Further, location and distribution regularity including the occurrence time of plastic hinges are fully recognized. Results show that (1) The effect of soil and artificial boundary on structural response is significant and not be ignored; (2) The plastic hinges distribution regulation and failure mode are very sensitive to uniform and multiple-point earthquake motions input; (3) The influence of pseudo-static and dynamic action is respectively due to the uniformity and frequency-spectrum character of earthquake motions at different support. (4) The plasticity response is more sensitive to contact-nonlinearity and cause more severe failures.

Keywords: sea-crossing bridge; visco-elastic artificial boundary conditions; multiple-point earthquake motions; plastic hinges; failure mode; pseudo-static

## 0 引 言

通过数值分析事先了解强震激励下弹塑性和抗倒塌性能，是防御结构体系倒塌和保障其正常服役的有效途径，而数值模型考虑因素的全面性与可靠性是基本前提之一。

本文建立大跨海床地基-桩-墩-悬索桥结构体系的有限元模型。模型包括模拟透射边界的粘弹性人工边界、大变位几何非线性效应的悬链线索找形，考虑了摩尔-库伦准则的地基土本构、摩擦效应的桩-土接触非线性以及钢筋和混凝土滞回耗能效应的材料非线性。首先，分别考察水动附加质量和人工边界对结构体系自身模态的影响，对考虑这两种因素与否的三种数值模型进行分析，对本文后续的结构地震反应分析起到指导作用。然后，根据实际情况生成目标场地对应的地基位置的多点地震动。最后，进行地震弹塑性分析。然后，性质上重点考察了构件塑性铰首现位置、逐渐发展和分布规律对地震动的空间变异性，人工边界条件和接触非线性的敏感性；进而，分析了拟静力反应对于结构总反应的比例，并深入认识拟静力和动力作用对于结构体系塑性铰的出现时间、位置及其分布规律的各自贡献。同时，还通过大量分析，考察了地震动峰值、持时以及接触非线性对结构塑性发展和倒塌模式的影响。

作为该项工作的第II部分，本文从实际工程角度不仅验证了I部分工作的实用性和可靠性，而且考察内容和分析结果和建议具有实用性建设性，可对类似工程直接提供有益参考。

## 1 数值模型建立与模态分析

### 1.1 数值模型建立与非线性因素

### 1.2 模态分析与对比

## 2 场地土与多点地震动

### 2.1 场地参数

### 2.2 多点地震动

## 3 弹塑性的时频两域计算与敏感参数分析

### 3.1 地震动空间变异性的影响

### 3.2 地震动峰值和持时的影响

### 3.3 接触非线性的影响

## 4 拟静力与动力作用的贡献与影响

## 5 结语

## 参考文献:

[1] Alejandro Asfura, Armen Der Kiureghian. Floor response spectrum method for seismic analysis of multiply supported secondary systems[J]. Earthquake Engineering & Structural Dynamics, 1985,14(2): 245-265.

[2] Yamamura N, Tanaka H. Response analysis of flexible MDF systems for multiple-support seismic excitations[J]. Earthquake

Engineering &Structural Dynamics, 1990, 19: 345-357

[3] Berrah.M, Kausel E. Response spectrum analysis of structures subjected to spatially varying motions[J]. Earthquake Engineering & Structural Dynamics, 1992, 21(6): 461-470

[4] Berrah.M, Kausel E. A modal combination rule for spatially varying seismic motions[J]. Earthquake Engineering &Structural

Dynamics, 1993, 22(9): 791-800

[5] Armen Der Kiureghian, Ansgar Neuenhofer. Response spectrum method for multi-support seismic excitations[J]. Earthquake Engineering & Structural Dynamics, 1992,21(8): 713-740.

[6] Chin-Hsiung Loh and Bao-Ding Ku. An efficient analysis of structural response for multiple-support seismic excitations[J].

Engineering Structures, 1995,17(1): 15-26

[7] Kahan M., Gibert R. Influence of seismic waves spatial variability on bridges: a sensitivity analysis. [J]. Earthquake Engineering & Structural Dynamics, 1996,25(8): 795-814.

[8] 王君杰. 多点多维地震动随机模型及结构的反应谱分析[D]. 哈尔滨：国家地震局工程力学研究所，1992.

Wang Junjie. Stochastic model of multi-component multi-support seismic motion and structural response spectrum analysis[D].Harbin: Institute of  Engineering Mechanics of State Seismological Bureau,1992.

[9] 李杰，李建华. 多点地震激励下结构随机地震反应分析的反应谱法[J].地震工程与工程振动，2004，24（3）：21-29

Li Jie, Li Jianhua. A response spectrum method for random vibration analysis of structures under multi-support excitation[J]. Earthquake Engineering and Engineering Vibration, 2004，24（3）：21-29

[10] 刘先明，叶继红，李爱群. 多点输入反应谱法的理论研究.土木工程学报，2005，38（3）：17-22.

Liu Xianming, Ye Jihong, Li Aiqun. Research of multi-support response spectrum method[J]. China Civil Engineering Journal, 2005,38(3):17-22.

[11] 孙建梅，叶继红，程文穰. 多点输入下大跨空间网格结构的可靠度分析[J].应用力学学报, 2005, 22(4):560-566.

[12] 叶继红,孙建梅..多点激励反应谱法的理论研究[J]. 应用力学学报,2007,24(1). 47-53

Ye Jihong ,Sun Jianmei. Response spectrum method for multi-support seismic excitation. Chinese Journal of applied mechanics, 2007,24(1). 47-53

[13] 苏亮.大跨空间结构的多点反应谱法和多点地震反应性状的研究（博士后研究工作报告）.浙江：浙江大学

[14] Edward L. Wilson. Three-dimensional static and dynamic analysis of structures: A physical approach with emphasis on earthquake engineering[M]. California: Computers and Structures, Inc. 2004

[15] 柳国环,李宏男,林海.结构地震响应计算模型的比较与分析[J].工程力学, 2009，26(2)：10–15

Liu Guohuan, Li Hongnan, Lin Hai. Model comparision and analysis for structural seismic response[J]. Engineering Mechanics. 2009，26(2)：10–15 (in chinese).

[16] 柳国环,李宏男,国巍.求解结构地震响应位移输入模型存在的问题及其AMCE实效对策[J]. 计算力学学报，2009，26(6)：862–869.

Liu Guohuan , Li Hongnan, Guo wei. Existing problem of displacement input model for calculating structural responses under earthquake ground motion and its an actual effective solution method called AMCE[J]. Chinese Journal. of Computational Mechanics2009，26(6)：862–869.（in chinese）

[17] 柳国环,李宏男,国巍等.求解结构地震响应位移输入模型中存在问题的一种新解决方法[J]. 工程力学, 2010，27(9):

55-62.

Liu Guohuan , Li Hong nan , Guo Wei, Tian-Li . A new method for solving existing problem of current displacement

input model for calculating structural seismic responses[J]. Engineering Mechanics, 2010, 27(9): 55–62.（in chinese）

[18] 柳国环,李宏男,田利.九江长江大桥在多点多维地震激励下的反应分析[J]. 振动与冲击, 2009,28(9):204-209

Liu Guohuan , Li Hong nan, Tian Li . Response analysis of JIUJIANG Yangtze River highway bridge under spatially

variable earthquake ground motions[J]. Journal of Vibration and Shock, 2009,28(9): 204-209（in chinese）

[19] 柳国环，陆新征. 基岩地震谱与地震动位移输入的土–结构相互作用(SSI)计算模型改进[J]. 岩石力学与工程学报,

2012, 29(4): 2011, 30(5): 884-892

Liu Guohuan, Lu Xinzheng. Spectra of bedrock earthquake motion and improvement of soil-structure interaction (SSI)

calculation model for seismic displacement inputting[J], Chinese Journal of Rock Mechanics and Engineering, 2011, 30(5): 884-892（in chinese）

[20] Annil K. Chopra著. 谢礼立，吕大刚译.结构动力学理论及其在地震工程中的应用[M].（第2版）北京：科学出版社, 2010,11

Annil K. Chopra. Xie Lili, Lv Dagang. Dynamics of structures theory and applications to earthquake engineering[M]. (second edition) Beijing: Higher Education Press, 2010,11（in chinese）

[21] 柳国环，陆新征，国巍，等.主跨300米级独塔斜拉桥考虑地震动多点激励与材料应变率效应的弹塑性分析[J]. 计算力学学报,(录用待发表)

Liu Guohuan, Lu Xinzheng, Guo Wei. Study of steel strain-rate and multiple earthquake motions effect on elasto-plasticity responses of 300m span single tower cable-stayed bridge[J]. Chinese Journal.of Computational Mechanics,(accepted)

[23] 柳国环，陆新征，国巍. 基于震源机制且考虑场地土分层差异效应的多点地震动：理论与程序开发[J]. 计算力学学

报, 2012,29(4):582-588

Liu Guohuan, Lu Xinzheng, Guowei. Multi-point seismic motions based on focal mechanism and considering local site multi-layer soil effect： theory and program implementation[J]. Chinese Journal.of Computational Mechanics, 2012,29(4): 582-588（in chinese）

[25]柳国环, 等.多点反应谱模型存在的问题与注记[J]. 振动与冲击,（审稿中）

Liu Guohuan, etc. Defect and Notes on Multi-supported Response Spectrum Model[J], Journal of Vibration and Shock, (Under Review)

[24] Hao Hong, Oliveira C.S, J. Penzien. Multiple-station ground motion processing and simulation based on smart-1 array data[J] Nuclear Engineering and Design,1989, 111(3): 293-310